## Slide 1: Internet Protocol & Domain Name System
CSC 102 Lecture 2b
Nicholas R. Howe

## Slide 2: IP Packet Specifics
Header is usually 20 bytes long
  160 bits
  40 hexadecimal digits
Split into data fields of varying length
  TTL is bits 64-71
  Source IP is 96-127
  Destination IP is 128-159
Converter
01100010101110010110010001010011001101001001…
6 2 B 9 6 4 5 3 3 4 9…
32 bits/ 4 bytes / 8 hexadecimal digits
Header
Data

## Slide 3: Activities
Ping lab
Traceroute lab

## Slide 4: Address Availability
Q. 4 bytes in IP address. How many addresses?
A. 232 adresses, or about 4 billion
  Many allocated & unused (Smith has 65536)
  More internet capable devices (e.g., smartphones)
We are running out of IP addresses!
What can be done?
have run

## Slide 5: (Partial) Solution #1: DHCP
DHCP = Dynamic Host Configuration Protocol
  Each host requests local IP address from a pool
  Addresses are “leased” not “owned”
Internet
215.68.17.67
215.68.17.114
215.68.17.0
DHCP server hands out
IP addresses from a pool

## Slide 6: Solution #1: DHCP + NAT
NAT = Network Address Translation
  DHCP server has only “real” IP address
  Assigns fake addresses in special reserved blocks
  Alters addresses on inbound/outbound packets
Internet
192.168.1.1
192.168.1.2
215.68.17.0
(outward facing IP)
192.168.1.0
(inward facing IP)
Home routers offer DHCP with NAT
Notes:     192.168.X.X, 10.X.X.X, 172.16.0.0-172.31.255.255

## Slide 7: Solution #2: IPv6
New internet protocol uses 16 byte addresses
  2128 addresses: will we ever run out?
  Main problem: how to switch over

## Slide 8: Domain Names
Domain names: alternate host identification for human convenience (added in 1983)
Each valid domain string corresponds to some IP address representing a host
  TLD are categories (.com, .org) or countries (.us, .cn)
  Domains correspond to owners/entities (traditionally!)
  Subdomains at the discretion of each domain owner
cs.smith.edu
Top-level domain (TLD)
Domain
Subdomain

## Slide 9: Directory Name Service
DNS servers respond to request for IP addresses
Local DNS caches results from authoritative servers
Lab: nslookup
Root nameserver
[198.41.0.4]
Local DNS
Authoritative Sources
Client
“Where’s en.wikipedia.org?”
“.org?”

## Slide 10: Directory Name Service
DNS servers respond to request for IP addresses
Local DNS caches results from authoritative servers
Lab: nslookup
Root nameserver
[198.41.0.4]
Local DNS
.org nameserver
[204.74.112.1]
Authoritative Sources
Client
“Where’s en.wikipedia.org?”
“.org?”
“Ask 204.74.112.1”
“wikipedia.org?”

## Slide 11: Directory Name Service
DNS servers respond to request for IP addresses
Local DNS caches results from authoritative servers
Lab: nslookup
Root nameserver
[198.41.0.4]
Local DNS
.org nameserver
[204.74.112.1]
Authoritative Sources
Client
“Where’s en.wikipedia.org?”
“.org?”
“Ask 204.74.112.1”
“wikipedia.org?”
wikipedia.org nameserver
[207.142.131.234]
“Ask 207.142.131.234”
“en.wikipedia.org?”

## Slide 12: Directory Name Service
DNS servers respond to request for IP addresses
Local DNS caches results from authoritative servers
Lab: nslookup
Root nameserver
[198.41.0.4]
Local DNS
.org nameserver
[204.74.112.1]
wikipedia.org nameserver
[207.142.131.234]
“Ask 204.74.112.1”
“Ask 207.142.131.234”
“.org?”
“wikipedia.org?”
“en.wikipedia.org?”
“It’s at 207.142.131.234”
Authoritative Sources
Client
“Where’s en.wikipedia.org?”

## Slide 13: Directory Name Service
DNS servers respond to request for IP addresses
Local DNS caches results from authoritative servers
Lab: nslookup
Local DNS
Client
“Where’s en.wikipedia.org?”
Client 2
“It’s at 207.142.131.234”
Root nameserver
[198.41.0.4]
.org nameserver
[204.74.112.1]
wikipedia.org nameserver
[207.142.131.234]
Authoritative Sources

## Slide 14: Internet Governance
Early Internet developed by small group of interested parties
  Example: one man in charge of domain names!
  Government funded but gave little direction
  Mostly US control
With growth, pressure for more formal system
  Technical development
  Policy development
Vint Cerf & Bob Kahn
Jon Postel

## Slide 15: Technical Development
Standards developed through RFC process
  RFC = Request For Comment
  Initial drafts revised using community feedback
  After consensus, are adopted as standard
Began as informal, academic process
Now overseen by IETF/IESG (Internet Engineering Task Force/Steering Group)

## Slide 16: Internet Policy & Administration
ICANN formed 1998
IANA contracts with private registrars
IP addresses: 5 regional internet registries
Domain names: contractors run Network Information Centers
Retail registrars file with NIC for each domain
ICANN
International Corporation for Assigned Names and Numbers
IANA
Internet Assigned Numbers Authority
Domain Name Registrar
Domain Name Registrar
RIR
Regional Internet Registry
NIC
Network Information Center